PG Lifelink

167 Gap Way

Erlanger KY 41005

Phone: 800-287-4123

Phone: 859-283-5900

Fax: 859-372-6272

E-mail: sales@pglifelink.com

Website: www.pglifelink.com

SECTION 26 05 33

RACEWAY and boxes for electrical systems

GENERAL

SUMMARY

Section Includes: This Section specifies aluminum surface-mounted metal raceways.

Specifier Note: Revise Paragraph below to suit project requirements. Add section numbers and titles per CSI MasterFormat and specifier=s practice.

Related Requirements:

Specifier Note: Include in this Paragraph only those sections and documents that directly affect the work of this section. If a reader of this section could reasonably expect to find a product or component specified in this section, but it is actually specified elsewhere, then the related section number(s) should be listed in the Subparagraph below. Do not include Division 00 documents or Division 01 sections since it is assumed that all technical sections are related to all project Division 00 documents and Division 01 sections to some degree. Refer to other documents with caution since referencing them may cause them to be considered part of the Contract.

Section [______].

REFERENCES

Specifier Note: Paragraph below may be omitted when specifying manufacturer(s proprietary products and recommended installation. Retain References Paragraph when specifying products and installation by an industry reference standard. List retained standard(s) referenced in this section alphabetically. Indicate issuing authority name, acronym, standard designation and title. Establish policy for indicating edition date of standard referenced. Contract Conditions or Section 01 42 00 - References may establish the edition date of standards. This Paragraph does not require compliance with standard(s). It is a listing of all references used in this section. Only include here standards that are referenced in the body of the specification in PARTS 1, 2 and/or 3. Do not include references to building codes at any level.

Reference Standards:

ASTM International (ASTM):

ASTM B317 / B317M Standard Specification for Aluminum-Alloy Extruded Bar, Rod, Tube, Pipe, Structural Profiles, and Profiles for Electrical Purposes (Bus Conductor).

American National Standards Institute (ANSI) / Underwriters Laboratories (UL)

ANSI/UL 5, Surface Metal Raceways and Fittings.

ANSI/UL 5, Multi Outlet Assemblies

ADMINISTRATIVE REQUIREMENTS

Coordination: Coordinate work of this Section with work of other trades for proper time and sequence to avoid construction delays. Comply with Section [01 31 00 - Project Management and Coordination].

Specifier Note: Add additional text to specify unusual or detailed coordination requirements affecting the work results of this Section.

[______].

Preinstallation Meetings: Conduct preinstallation meeting [one week] prior to commencing [work of this Section] [and] [on-site installations] to verify project requirements, substrate conditions and coordination with other building subtrades, and to review manufacturer=s installation instructions and manufacturer=s warranty requirements. Comply with Section [01 31 19 - Project Meetings].

Specifier Note: Add additional text to describe requirements for meetings to coordinate products and techniques and to sequence related work for sensitive and complex items.

[______].

Sequencing: Sequence work of this section in accordance with Section [01 12 16 - Work Sequence] [and manufacturer=s written recommendations for sequencing construction operations].

Specifier Note: Specify additional text as required to describe the particular sequence of events required to coordinate work that must be done in sequence with, or at the same time as, work in another section.

[______].

Scheduling: Schedule work of this Section in accordance with Section [01 32 13 - Scheduling of Work].

Specifier Note: Specify additional text to include requirements for coordinating work that requires unusual scheduling with work of other sections.

[______].

Specifier Note: Article below includes submittal of relevant data to be furnished by Contractor before, during or after construction. Coordinate this article with Architect=s and Contractor=s duties and responsibilities in Contract Conditions and Section 01 33 00 - Submittal Procedures.

ACTION SUBMITTALS

General: Submit listed submittals in accordance with Contract Conditions and Section [01 33 00 - Submittal Procedures].

Product Data: Submit specified products as follows:

Manufacturer's product data.

Catalog pages illustrating products to be incorporated into project.

Material Safety Data Sheets (MSDS), if applicable.

Shop Drawings: Indicate information on shop drawings as follows:

Layout of raceways indicating series being provided and accessories.

INFORMATION SUBMITTALS

Specifier Note: Specify submittal of test reports or evaluation service reports intended to document required tests without repeating the test requirements specified in Division 01.

General: Submit listed submittals in accordance with Contract Conditions and Section [01 33 00 - Submittal Procedures].

Test and Evaluation Reports:

Certified test reports showing compliance with specified performance characteristics and physical properties

Specifier Note: Specify submittals intended to document manufacturer installation, storage and other instructions.

Manufacturer=s Instructions: Submit manufacturer=s installation instructions.

Source Quality Control: Submit documentation verifying that components and materials specified in this Section are from single manufacturer.

QUALITY ASSURANCE

Qualifications:

Raceway Manufacturer:

Having [5] years of experience manufacturing components similar to or exceeding requirements of project.

Having sufficient capacity to produce and deliver required materials without causing delay in work.

Installer: Acceptable to the manufacturer, experienced in performing work of this section and has specialized in installation of work similar to that required for this project.

Specifier Note: Retain the following Paragraph when certification related to sustainability submittals is a project requirement.

Sustainability Standards Certification: Provide certification for [______] materials certified by [certification organization’s name] in accordance with [certification organizations standard].

DELIVERY, STORAGE & HANDLING

Delivery and Acceptance Requirements:

Deliver material in accordance with Section [01 61 00 - Common Product Requirements] and in accordance with manufacturer’s written instructions.

Deliver materials in manufacturer’s original packaging with identification labels intact and in sizes to suit project.

Storage and Handling Requirements:

Store materials protected from exposure to harmful weather conditions and at temperature conditions recommended by manufacturer.

Packaging Waste Management:

Specifier Note: The disposal of packaging waste into landfill sites demonstrates an inefficient use of natural resources and consumes valuable landfill space. Specifying appropriate packaging and construction waste management and disposal procedures may contribute to points required for USGBC’s LEED® construction project certification.

Specifier Note: Include the following Subparagraphs to specify information that will provide direction to the Contractor for the disposal of construction waste materials using environmentally responsible methodology other than landfill resources.

Separate waste materials for [reuse] [and] [recycling] in accordance with Section [01 74 19 - Construction Waste Management and Disposal].

Specifier Note: USGBC’s LEED( certification includes credits for the diversion of construction waste from landfill. Diversion can be tracked by either weight or volume but must be consistent for all materials.

Remove packaging materials from site and dispose of at appropriate recycling facilities.

Collect and separate for disposal [paper] [plastic] [polystyrene] [corrugated cardboard] packaging material [in appropriate onsite bins] for recycling.

Fold metal and plastic banding, flatten and place in designated area for recycling.

Specifier Note: Add additional Subparagraphs to include pallets, crates, padding and other packing materials that are typically associated with the specified products.

Remove:

Pallets from site.

[______].

PRODUCTS

Specifier Note: Retain Article below for proprietary method specification. Add product attributes, performance characteristics, material standards and descriptions as applicable. Use of such phrases as “or equal,”  “or approved equal” or similar phrases may cause ambiguity in specifications. Such phrases require verification (procedural, legal and regulatory) and assignment of responsibility for determining “or equal” products.

ALUMINUM SURFACE-MOUNTED METAL RACEWAYS

Specifier Note: Include in the following Paragraph manufacturer’s name, address, phone number, fax number, e-mail address and website URL.

Manufacturer: PG Lifelink.

Contact: 167 Gap Way, Erlanger KY 41005; Telephone: 800-287-4123, 859-283-5900, Fax: 859-372-6272; E-mail: sales@pglifelink.com; Website: www.pglifelink.com.

Specifier Note: Substitution procedures must appear either be in the Contract Conditions or in Section 01 25 00 - Substitution Procedures. Do not include substitution procedures here.

Single Source Responsibility: Provide components and materials specified in this section from a single manufacturer.

Substitution Limitations:

Substitutions: [In accordance with [Contract Conditions] [Section 01 25 00 - Substitution Procedures] [No substitutions permitted].

Specifier Note: Include an overall description of the system, assembly, product or material. Include required properties or characteristics that do not obviously belong under other titles. Examples: Configuration, size and color.

Description:

Specifier Note: Paragraph below should list obligations for compliance with specific code requirements particular to this section. General statements to comply with a particular code are typically addressed in Contract Conditions and Section 01 41 00 - Regulatory Requirements. Repetitive statements should be avoided.

Regulatory Requirements:

In accordance with Section [01 41 00 - Regulatory Requirements].

[______].

Sustainability Characteristics:

[______].

Compatibility:

Ensure components and materials are compatible with specified accessories and adjacent materials.

Specifier Note: Performance characteristics are usually stated with some form of evaluation or verification. Performance usually, but not universally, applies to systems and assemblies. Performance criteria can include structural, safety, fire resistance, vapor retardancy, acoustical, thermal, operational capacity and durability data.

Performance Criteria:

Comply with UL 5.

Provide raceways with the Listing Mark of Underwriters Laboratories Inc. (UL).

Specifier Note: Retain series below to comply with project requirements.

Versa-Duct 130 series:

Type: Single channel, single cover.

Size: 1 3/4 × 2 3/4 inches (44 × 70 mm).

Specifier Note: Series 130 can be configured in lengths from 1 ft to 1000 ft.

Length, Ft: [_____] [As indicated on the drawings].

Device Mounting: [Body] [Cover].

Receptacle Specification: [Hospital grade] [Spec grade].

Receptacle Quantities:

Duplex: [_____].

GFI: [_____].

Simplex: [_____].

Lab Services: [Devices] [Provisions].

Communication Quantity: [_____].

Water Saver Connector Fitting Quantity: [_____].

Specifier Note: Select cover length below; custom cut cover lengths are available.

Covers: [12] [18] [24] [_____] inches in length, snap-in type.

Finish: Satin anodized, standard.

Options:

Specifier Note: Retain options below to meet project requirements.

Powder coat finish, color to match architect’s sample.

Custom design as indicated on the drawings.

Versa-Duct 155 Series:

Type: Single channel, single cover.

Size: 1 3/4 × 2 3/4 inches (44 × 70 mm).

Specifier Note: Series 155 can be configured in lengths from 1 ft to 1000 ft.

Length, Ft: [_____] [As indicated on the drawings].

Device Mounting: [Body] [Cover].

Receptacle Specification: [Hospital grade] [Spec grade].

Receptacle Quantities:

Duplex: [_____].

GFI: [_____].

Simplex: [_____].

Lab Services: [Devices] [Provisions].

Communication Quantity: [_____].

Water Saver Connector Fitting Quantity: [_____].

Specifier Note: Select cover length below, custom cut cover lengths are available.

Covers: [12] [18] [24] inches in length, snap-in type.

Finish: Satin anodized, standard.

Options:

Specifier Note: Retain options below to meet project requirements.

Powder coat finish, color to match architect’s sample.

Custom design as indicated on the drawings.

Versa-Duct 250 Series:

Type: Dual channel, single cover.

Size: 2 1/4 × 4 3/4 inches (57 × 121 mm).

Specifier Note: Series 250 can be configured in lengths from 1 ft to 1000 ft.

Length, Ft: [_____] [As indicated on the drawings].

Device Mounting: [Body] [Cover].

Receptacle Specification: [Hospital grade] [Spec grade].

Receptacle Quantities:

Duplex: [_____].

GFI: [_____].

Simplex: [_____].

Lab Services: [Devices] [Provisions].

Communication Quantity: [_____].

Water Saver Connector Fitting Quantity: [_____].

Specifier Note: Select cover length below; custom cut cover lengths are available.

Covers: [12] [18] [24] inches in length, snap-in type.

Finish: Finish: Satin anodized, standard.

Options:

Specifier Note: Retain options below to meet project requirements.

Powder coat finish, color to match architect’s sample.

Custom design as indicated on the drawings.

Versa-Duct 252 Series:

Specifier Note: Series 252 can be configured in lengths from 1 ft to 1000 ft.

Type: Dual channel, dual cover.

Size: 2 1/4 × 5 1/4 inches (57 × 133 mm).

Length, Ft: [_____] [As indicated on the drawings].

Device Mounting: [Body] [Cover].

Receptacle Specification: [Hospital grade] [Spec grade].

Receptacle Quantities:

Duplex: [_____].

GFI: [_____].

Simplex: [_____].

Lab Services: [Devices] [Provisions].

Communication Quantity: [_____].

Water Saver Connector Fitting Quantity: [_____].

Specifier Note: Select cover length below, custom cut cover lengths are available.

Covers: [12] [18] [24] inches in length, snap-in type.

Finish: Finish: Satin anodized, standard.

Options:

Specifier Note: Retain options below to meet project requirements.

Powder coat finish, color to match architect’s sample.

Custom design as indicated on the drawings.

Versa-Duct 255 Series:

Type: Dual channel, dual cover.

Size: 2 1/2 × 6 inches (64 × 152 mm).

Specifier Note: Series 255 can be configured in lengths from 1 ft to 1000 ft.

Length, Ft: [_____] [As indicated on the drawings].

Device Mounting: [Body] [Cover].

Receptacle Specification: [Hospital grade] [Spec grade].

Receptacle Quantities:

Duplex: [_____].

GFI: [_____].

Simplex: [_____].

Lab Services: [Devices] [Provisions].

Communication Quantity: [_____].

Water Saver Connector Fitting Quantity: [_____].

Specifier Note: Select cover length below; custom cut cover lengths are available.

Covers: [12] [18] [24] inches in length, snap-in type.

Finish: [Satin anodized] [Powder coat, color to match Architect(s sample].

Options:

Specifier Note: Retain options below to meet project requirements.

Powder coat finish, color to match architect’s sample.

Custom design as indicated on the drawings.

Versa-Duct 345 Series:

Type: Triple channel, dual cover.

Size: 2 1/4 × 7 1/2 inches (57 × 190 mm).

Specifier Note: Series 345 can be configured in lengths from 1 ft to 1000 ft.

Length, Ft: [_____] [As indicated on the drawings].

Device Mounting: [Body] [Cover].

Receptacle Specification: [Hospital grade] [Spec grade].

Receptacle Quantities:

Duplex: [_____].

GFI: [_____].

Simplex: [_____].

Lab Services: [Devices] [Provisions].

Communication Quantity: [_____].

Water Saver Connector Fitting Quantity: [_____].

Specifier Note: Select cover length below; custom cut cover lengths are available.

Covers: [12] [18] [24] inches in length, snap-in type.

Finish: Finish: Satin anodized, standard.

Options:

Specifier Note: Retain options below to meet project requirements.

Powder coat finish, color to match architect’s sample.

Custom design as indicated on the drawings.

Materials:

6063-T5 extruded aluminum, ASTM B317.

Power Devices: Provide brackets and screws for mounting to raceway or raceway cover.

Wiring:

Type: THHN stranded

Gauge: 15 amp #14, 20 amp #12, 30 amp #10, 50 amp #6 and 60 amp #4.

Grounding: When isolated ground receptacles are indicated on the drawings, provide a separate green insulating grounding conductor connected only to the receptacle terminal.

Connection Pigtails: 12 inch receptacle pigtails.

Fabrication:

Provide pre-cut, pre-wired and pre-assembled raceways as indicated.

Provide relief slots on either side for cover removal and accessibility.

Labels:

Front of Raceway:

Provide for each receptacle a label indicating panel circuit numbers.

Provide for each receptacle over 125V an additional label indicating voltage, phase and amperage.

Back of Raceway:

Provide label indicating raceway number and room/area.

ACCESSORIES

Specifier Note: Retain accessories below to comply with project requirements.

Elbows: Provide types and quantities indicated for each series specified.

Type(s): [Regressed inside] [Mitered flat] [Flat tee] [Mitered outside].

Quantities: As indicated on the drawings.

SOURCE QUALITY CONTROL

Specifier Note: Describe each test to be conducted. Include test method, sampling requirements, observation by independent authorities (if any) and reporting requirements. Describe each inspection to be conducted, including method, personnel and reporting requirements.

Tests and Inspections:

Specifier Note: Describe specific requirements for coordinating special inspections, such as providing access to authorities having jurisdiction or other third parties.

Manufacturer Services.

[______].

EXECUTION

EXAMINATION

Verification of Conditions: Verify that conditions of substrates previously installed under other sections or contracts are acceptable for product installation in accordance with manufacturer’s instructions prior to aluminum metal raceway installation.

Inform [Owner] [Architect] [Consultant] of unacceptable conditions immediately upon discovery.

Proceed with installation only after unacceptable conditions have been remedied [and after receipt of written approval from [Owner] [Architect] [Consultant]].

[______].

Specifier Note: Specify actions required to prepare the surface, area or site for incorporation of the section(s primary products. Describe requirements for exposure or removal of existing assemblies, components, products or materials.

PREPARATION

Specifier Note: Specify preparatory work required prior to installation/application/erection of primary products.

Ensure structure or substrate is adequate to support aluminum surface-mounted metal raceways.

[______].

Specifier Note: Specify preparatory work, such as selective removal of existing work, required prior to execution of new work. Specify requirements for exposure or removal of existing assemblies, components, products or materials.

Demolition/Removal:

[______].

INSTALLATION

Coordinate installation of aluminum metal raceways in accordance with Section [01 73 19 - Installation].

Coordinate aluminum metal raceway work with work of other trades for proper time and sequence to avoid construction delays.

Install aluminum metal raceways plumb and level, unless indicated otherwise.

Accurately fit, align, securely fasten and install free from distortion or defects.

CLEANING

Perform cleanup in accordance with Section [01 74 00 - Cleaning and Waste Management] and Section [01 74 13 - Progress Cleaning].

Upon completion, remove surplus materials, rubbish, tools and equipment in accordance with Section [01 74 23 - Final Cleaning].

Specifier Note: Specify special measures needed to minimize waste, collect recyclable waste and dispose of or recycle field-generated construction waste created during demolition, construction or final cleaning.

Waste Management:

Coordinate recycling of waste materials with Section [01 74 19 - Construction Waste Management and Disposal].

Collect recyclable waste and dispose of or recycle field generated construction waste created during demolition, construction or final cleaning.

Remove recycling containers and bins from site.

[______].

Specifier Note: Specify protection methods completed after installation, but prior to acceptance by the owner. Protection of surrounding areas and surfaces during application or installation is included under PART 3, Preparation. Include only statements unique to this Section.

Specifier Note: Coordinate the following Article with Section 01 76 00 - Protecting Installed Construction.

PROTECTION

Protect installed product from damage during construction in accordance with Section [01 76 00 - Protecting Installed Construction].

Repair damage to adjacent materials caused by [insert section subject matter] installation.

[______].

Specifier Note: Specify attachments such as schedules, tables, illustrations or forms in this location if they are not incorporated directly within the specification text.

ATTACHMENTS

Specifier Note: Schedules are sometimes placed in the specifications rather than on the drawings. Include schedules that indicate item/element/product/equipment, location and other coordinating data.

Schedules:

[______].

END OF SECTION